FAQ*: WFCM Checklist

Question: I understand if a new home is built in a town in a 110 mph wind zone then the American Forest and Paper Association (AF&PA) Wood Frame Construction Manual can be used to prescriptively design it. I also understand that in some cases the home can be framed per the WFCM 100 mph Guide, if it meets certain requirements including but not limited to aspect ratio, roof height, number of stories, and exposure category (B). I have heard that Massachusetts has a “modified” checklist that can be used instead of the checklist at the end of the Guide. Is this true and what can you tell me about this “modified” checklist?

Answer: You are correct on the items that you have noted. MA has modified the checklist in several important ways. The MA version allows a roof with a pitch up to and including 8 in 12 to not be “counted” as a story. Further it does not require steel hold downs and straps in many locations if full height sheathing is used as defined in the MA checklist. Further, if the building will have furring strips installed in the ceiling abutting the gable wall then 2 x 4s installed on top of the ceiling joists are not required. There are other changes as well that were not noted here.

The MA version of the checklist was formulated in recognition of the highly regarded framing methods used in MA for many years and wood framing that has been used in North Carolina over the past 10 to 15 years which has performed well in severe hurricane weather in that state.

* Answers to FAQs are opinions of the BBRS Staff and do not reflect official positions or code interpretations of the BBRS.

( Check

Compliance

1.1  SCOPE

Wind Speed (3-sec. gust)		110  mph	____

Wind Exposure Category		B	____

1.2  APPLICABILITY

Number of Stories (a roof which exceeds 8 in 12 slope shall be considered a story) 	_____ stories  ≤ 2 stories	____

Roof Pitch 	(Fig 2) 	_____  ≤ 12:12	____

Mean Roof Height 	(Fig 2)	___ ft  ≤ 33’	____

Building Width, W 	(Fig 3)	 ___ ft  ≤ 80’	____

Building Length, L 	(Fig 3)	___ ft  ≤ 80’	____

Building Aspect Ratio (L/W) 	(Fig 4)	_____ ≤ 3:1	____

Nominal Height of Tallest Opening2 	(Fig 4)	_____ ≤ 6’8”	____

1.3  FRAMING CONNECTIONS

General compliance with framing connections	(Table 2)		____

2.1  FOUNDATION

Foundation Walls meeting requirements of 780 CMR 5404.1

Concrete………………………………………………………………………………………………………………	____

Concrete Masonry ……..			____

2.2  ANCHORAGE TO FOUNDATION1,3

5/8” Anchor Bolts imbedded or 5/8” Proprietary Mechanical Anchors as an alternative in concrete only

Bolt Spacing – general ……………………………	(Table 4)	  _____ in.	____

Bolt Spacing from end/joint of plate 	(Fig 5)	_____ in. ≤ 6” – 12”	____

Bolt Embedment – concrete	(Fig 5)…...	.___ in. ≥ 7”   	____

Bolt Embedment – masonry	(Fig 5)	_____ in. ≥ 15”	____

Plate Washer	(Fig 5)	≥ 3” x 3” x ¼”	____

3.1  FLOORS

Floor framing member spans checked 	(per 780 CMR Chapter 55)		____

Maximum Floor Opening Dimension	(Fig 6)	___ ft ≤ 12’ 	____

Full Height Wall Studs at Floor Openings less than 2’ from Exterior Wall (Fig 6)…………………………………              ____

Maximum Floor Joist Setbacks

Supporting Loadbearing Walls or Shearwall	(Fig 7)	___ ft  ≤ d	____

Maximum Cantilevered Floor Joists

Supporting Loadbearing Walls or Shearwall	(Fig 8)	___ ft  ≤ d	____

Floor Bracing at Endwalls	(Fig 9)		____

Floor Sheathing Type 		(per 780 CMR Chapter 55)		____

Floor Sheathing Thickness 	(per 780 CMR Chapter 55)	____ in.	____

Floor Sheathing Fastening	(Table 2)	___d nails at ____in edge / ___ in field	____

4.1  WALLS

Wall Height

Loadbearing walls	(Fig 10 and Table 5)	___ ft  ≤ 10’	____

Non-Loadbearing walls	(Fig 10 and Table 5)	___ ft  ≤ 20’	____

Wall Stud Spacing		(Fig 10 and Table 5)	___ in. ≤ 24” o.c.	____

Wall Story Offsets		(Figs 7 & 8)	___ ft  ≤ d	____

4.2  EXTERIOR WALLS3

Wood Studs

Loadbearing walls	(Table 5)	2x___ - ___ ft ___ in. 	____

Non-Loadbearing walls	(Table 5)	2x___ - ___ ft ___ in. 	____

Gable End Wall Bracing 1

Full Height Endwall Studs	(Fig 10)		____

WSP Attic Floor Length	(Fig 11)	____ ft ≥W/3	____

Gypsum Ceiling Length (if WSP not used)	(Fig 11)	___ ft ≥ 0.9W 	____

and 2 x 4 Continuous Lateral Brace @ 6 ft. o.c. .. (Fig 11)…………………………		____

or 1 x 3 ceiling furring strips @ 16” spacing min. with 2 x 4 blocking @ 4 ft. spacing in end joist or truss bays____

Double Top Plate

Splice Length		(Fig 13 and Table 6)	___ ft 	____

Splice Connection (no. of 16d common nails)	(Table 6)	___	____

Loadbearing Wall Connections

Lateral (no. of 16d common nails)	(Tables 7)	____	____

Non-Loadbearing Wall Connections

Lateral (no. of 16d common nails)	(Table 8)	____	____

Load Bearing Wall Openings (record largest opening but check all openings for compliance to Table 9)

Header Spans		(Table 9)	___ ft ___ in. ≤ 11’	____

Sill Plate Spans		(Table 9)	___ ft ___ in. ≤ 11’	____

Full Height Studs	(no. of studs)	(Table 9)	____	____

Non-Load Bearing Wall Openings (record largest opening but check all openings for compliance to Table 9)

Header Spans……	(Table 9)	___ ft ___ in. ≤ 12’	____

Sill Plate Spans….	(Table 9)	___ ft ___ in. ≤ 12”	____

Full Height Studs (no. of studs)	(Table 9)	____	____

Exterior Wall Sheathing to Resist Uplift and Shear Simultaneously4

Minimum Building Dimension, W

Nominal Height of Tallest Opening2   ……………................................................................___≤ 6’8”        ____

Sheathing Type	(note 4)	______	____

Edge Nail Spacing	(Table 10 or note 4 if less)	____ in. 	____

Field Nail Spacing	(Table 10)	____ in. 	____

Shear Connection (no. of 16d common nails)	(Table 10)	___	____

Percent Full-Height Sheathing	(Table 10)	___%	____

5% Additional Sheathing for Wall with Opening > 6’8” (Design Concepts)		____

Maximum Building Dimension, L

Nominal Height of Tallest Opening2.......	………………………………………………....___≤ 6’8”         ____

Sheathing Type	(note 4)	______	____

Edge Nail Spacing	(Table 11 or note 4 if less)	____ in. 	____

Field Nail Spacing	(Table 11)	____ in. 	____

Shear Connection (no. of 16d common nails)	(Table 11)	___	____

Percent Full-Height Sheathing	(Table 11)	___%	____

5% Additional Sheathing for Wall with Opening > 6’8” (Design Concepts)		____

Wall Cladding

Rated for Wind Speed?			____

5.1  ROOFS

Roof framing member spans checked?	(For Rafters use AWC Span Tool, see BBRS Website)	____

Roof Overhang		(Figure 19)	___ ft ≤ smaller of 2’ or L/3	____

Truss or Rafter Connections at Loadbearing Walls

Proprietary Connectors

Uplift	(Table 12)	U=____ plf	____

Lateral	(Table 12)	L=____ plf	____

Shear	(Table 12)	S=____ plf	____

Ridge Strap Connections, if collar ties not used per page 21… (Table 13)	T=____ plf	____

Gable Rake Outlooker	(Figure 20)	___ ft ≤ smaller of 2’ or L/2	____

Truss or Rafter Connections at Non-Loadbearing Walls

Proprietary Connectors

Uplift	(Table 14)	U=____ lb.	____

Lateral (no. of 16d common nails)	(Table 14)………………………………...L =___	_lb.             ____

Roof Sheathing Type	(per 780 CMR Chapters 58 and 59)	 …………                    ____

Roof Sheathing Thickness		___ in. ≥ 7/16” WSP	____

Roof Sheathing Fastening	(Table 2)	___	____

Notes:

- This checklist shall be met in its entirety, excluding the specific exception noted in 2, to comply with the requirements of 780 CMR 5301.2.1.1 Item 1. If the checklist is met in its entirety then the following metal straps and hold downs are not required per the WFCM 110 mph Guide:

  - Steel Straps per Figure 5

  - 20 Gage Straps per Figure 11

  - Uplift Straps per Figure 14

  - All Straps per Figure 17

  - Corner Stud Hold Downs per Figure 18a and Figure 18b

- Exception: Opening heights of up to 8 ft. shall be permitted when 5% is added to the percent full-height sheathing requirements shown in Tables 10 and 11.

- The bottom sill plate in exterior walls shall be a minimum 2 in. nominal thickness pressure treated #2-grade.

  - From Tables 10 and 11 and location of wall sheathing and Building Aspect Ratio, determine Percent Full-Height Sheathing and Nail Spacing requirements

  - Wood Structural Panels shall be minimum thickness of 7/16” and be installed as follows:

    - Panels shall be installed with strength axis parallel to studs.

    - All horizontal joints shall occur over and be nailed to framing.

    - On single story construction, panels shall be attached to bottom plates and top member of the double top plate.

    - On two story construction, upper panels shall be attached to the top member of the upper double top plate and to band joist at bottom of panel. Upper attachment of lower panel shall be made to band joist and lower attachment made to lowest plate at first floor framing.

    - Horizontal nail spacing at double top plates, band joists, and girders shall be a double row of 8d staggered at 3 inches on center per figures below : Vertical and Horizontal Nailing for Panel Attachment